## Slide 1: I2c - SPI
Christian Ritz, ritzc2@bfh.ch

## Slide 2: I2C = TWI
http://www.engineersgarage.com/tutorials/twi-i2c-interface

## Slide 3: I2C
Small distances between IC
Max 128 Slaves
One or more Masters
Speed
  100 kbit/s = Standard
  400 kbit/s = Fast mode
  3,4 MBit/s = High-speed mode
  5,0 MBit/s = Ultra fast mode (Unidirectional)
Reduce speed for large distance transmissions

## Slide 4: I2C - Address
http://i2c.info/i2c-bus-specification

## Slide 5: I2C – Protocol
http://i2c.info/i2c-bus-specification

## Slide 6: I2C – Protocol
Single message where a master writes data to a slave;
Single message where a master reads data from a slave;
Combined messages, where a master issues at least two reads and/or writes to one or more slaves.

## Slide 7: I2C – Protocol
Single message where a master writes data to a slave;
http://i2c.info/i2c-bus-specification

## Slide 8: I2C – Protocol
Single message where a master reads data from a slave;
http://i2c.info/i2c-bus-specification

## Slide 9: I2C – Protocol
Combined messages, where a master issues at least two reads and/or writes to one or more slaves.
http://i2c.info/i2c-bus-specification

## Slide 10: I2C - Demo

## Slide 11: SPI
Serial Peripheral Interface

## Slide 12: SPI - Modes
Mode | CPOL (Clock polarity) | CPHA (Clock phase)
0 | 0 | 0
1 | 0 | 1
2 | 1 | 0
3 | 1 | 1
CPOL = 0 Clock idle low
CPOL = 1 Clock idle high
CPHA = 0 Data taken on first flank after SS
CPHA = 1 Data taken on second flank after SS